## Slide 1: PiezoMEMS Design for Test
Joe Evans, Naomi Montross, Spencer Smith, Bob Howard, Scott Chapman
Radiant Technologies, Inc.
2019 International Workshop on Piezoelectric MEMS
July 16, 2019

## Slide 2
Radiant has long considered what test instruments and procedures will be needed to characterize piezoMEMS. Certainly, a more complex test architecture is required than that for simple capacitors. New test procedures and specialized fixtures will both be necessary to reduce the time required to evaluate each design once it comes off the wafer. In turn, each pMEMS device must be designed to function within the new test architecture.
Summary

## Slide 3
Introduction
  Radiant is now generating devices from an in-house piezoMEMS process under development since 2008.
  Radiant is adding new infrastructure to its testers to evaluate these devices.

## Slide 4
Issues
    Some of the new devices contain five capacitors. Every capacitor on every device must be tested for its ferroelectric properties.
    New tests are needed to evaluate electromechanical properties.
    The devices will embed into their own control circuits in order to operate autonomously. Test hardware must now test circuits.
    The circuits must see elevated temperature to determine long-term reliability.
    Some sort of packaging is necessary to allow the pMEMS devices to be physically handled and inserted into circuit boards.
    Radiant put 38 different individual pMEMS and solid state device circuits on its development wafer. Every one of those dice must be characterized in order to make appropriate improvements to the process. Each device requires a different test board.

## Slide 5
    Traditional IC packages are expensive and require wire bonding.
    Packages may also interfere with the functionality of pMEMS sensors because the package isolates the sensor from its ambient environment.
    Radiant decided to discard traditional packages and solder dice directly onto PC boards.
    Old fashioned copper/gold solder pads on the die match SOIC solder pads on the PC board. The die flips over so the pMEMS is face down and looks out the underside of the die. The delicate parts of the MEMS are protected.
Packaging
Radiant uses an SOIC format with a 3.4mm x 3.4mm die floor plan.
Die Floor
Plan

## Slide 6
PiezoMEMS Tester
  To interface with analog/digital circuits surrounding the pMEMS, Radiant has added additional functions to the Precision Multiferroic tester to create the Precision PiezoMEMS tester.
  True LCR
  Digital I/O
  I2C communications
  DC Voltage Source for powering circuits.
  Frequency Counter
  Asynchronous Pulse Generator
  Asynchronous 16-bit Voltage Measurement
New Vision Tasks are being written: Impulse Response, Resonance Excitation, and Quality Factor determination.

## Slide 7
Impulse Response
  Below is the tip displacement of an Radiant 42mm e31 cantilever after an electrical Impulse event. FFT the polarization and the displacement traces.
Resonance = 311Hz

## Slide 8
Resonance Response
  Next, apply a continuous stimulus of small amplitude to the cantilever at its resonant frequency. Qm will cause the mechanical displacement to grow.
2nd Harmonic = 622Hz

## Slide 9
FWHM
~ 264
FWHM
Resonant Frequency
  The Quality Factor can be estimated from the FFT of the Resonance Curve. Divide the resonant frequency by its Full Width at Half Maximum in Hertz.

## Slide 10
Complete Test Sequence
  Consider this tuning fork, it has three capacitors. The following test sequence must be executed individually on all three capacitors of the die.
  Ferroelectric Polarization/Leakage/etc.
  Set the Poling direction for operation
  Impulse Response
  Resonance Response
  Quality Factor
  Insert device into its control circuit
  Track resonance with Frequency Counter.

## Slide 11
Consider a four-capacitor accelerometer. It will have four capacitors with five connections if all capacitors share a common ground.
Example Test Flow
Circuit diagram:
Proof Mass

## Slide 12
After fabrication, each capacitor should be tested in turn for shorts, hysteresis, & leakage. These are all classic ferroelectric tests.
Each capacitor is poled to its proper polarity and then tested for Impulse, Resonance, and Quality Factor if the device is to be a sensor.
Drive
Return
piezoMEMS Analyzer
Test Each Cap Individually

## Slide 13
After fabrication, each capacitor should be tested in turn for shorts, hysteresis, & leakage. These are all classic ferroelectric tests.
Each capacitor is poled to its proper polarity and then tested for Impulse, Resonance, and Quality Factor if the device is to be a sensor.
Drive
Return
piezoMEMS Analyzer
Test Each Cap Individually

## Slide 14
After fabrication, each capacitor should be tested in turn for shorts, hysteresis, & leakage. These are all classic ferroelectric tests.
Each capacitor is poled to its proper polarity and then tested for Impulse, Resonance, and Quality Factor if the device is to be a sensor.
Drive
Return
piezoMEMS Analyzer
Test Each Cap Individually

## Slide 15
After fabrication, each capacitor should be tested in turn for shorts, hysteresis, & leakage. These are all classic ferroelectric tests.
Each capacitor is poled to its proper polarity and then tested for Impulse, Resonance, and Quality Factor if the device is to be a sensor.
Drive
Return
piezoMEMS Analyzer
Test Each Cap Individually

## Slide 16
Radiant now has a dual 1:8 multiplexer that allows Vision to control all four capacitors from within a Test Definition.
A Mux Helps
Drive
Return
piezoMEMS Analyzer
Multiplexer
I2C

## Slide 17
The sample is inserted into its circuit which will control and amplify its signals. The circuit outputs are tested with the voltage sensing ports of the tester and with the new Frequency Counter.
Connect the Outer Circuit
V1
Sensor2
Sensor 1
piezoMEMS Analyzer
Power
PC Circuit Board

## Slide 18
Finally, the pMEMS and its circuit will be inserted into a temperature chamber for two days of testing at room temperature and 85C.
Into the Chamber
Sensor2
Sensor 1
piezoMEMS Analyzer
I2C/USB
V1
Power

## Slide 19
Radiant is developing two new test fixtures specialized for pMEMS and component level testing.
  The Low Voltage High Temperature Component Fixture
2. The Precision pMEMS Analyzer Test Matrix Board
Specialized Test Fixtures

## Slide 20
Prototype Component Fixture
Reliability testing of platinum-electrode PZT capacitors was previously reported by Radiant at the 2018 IWATMD Penn State meeting using this temperature chamber created out of extra parts at Radiant.
Dual capacitors in a single TO-18 package
Thermocouple
PNDS TO-18 Board
Original HVTF modified for optical heating.
Thermal Controller from the HVDM II
DRIVE/RETURN
USB
Power
I2C
PNDS 2-Channel Mux
Already tested packages

## Slide 21
Imprint Characterization
Simultaneous 85C opposite-state curves (red) for two capacitors for 24 hours. Results indicate potential >30 years imprint lifetime .
Blue = Retention
Red = Imprint
30 years
Retention Results: PZT never forgets!
From IWATMD 2018

## Slide 22
The LVH will be the commercial version of that original component thermal chamber.
The Low Voltage High Temperature Component Fixture brings all signals from the Precision piezoMEMS tester to a mother board inside a Teflon test chamber controlled from Vision.
  Rated temperature: 110C
LVH

## Slide 23
The Mother board inside the chamber has connectors that bring the signals to a Daughter board.
Radiant has its own general-purpose Daughter boards but a custom PCB can easily be fabricated to fit the Mother board for special dice.
LVH
The PCB with the pMEMS die is a “Baby” board.
Socket for Radiant’s Type AB packaged capacitors.

## Slide 24
The Matrix Board will have an array of unbuffered BNC input connectors and buffered BNC output connectors to allow signals to pass between the piezoMEMS Analyzer and a Device Under Test in the center of the board.
A relay matrix surrounding a central Daughter board will allow Vision to connect any pin of the pMEMS device package to any BNC or to a feedback path for the device.
In theory, any one of the 38 different die types on Radiant’s development wafer will be able to be inserted into the center Daughter board and have its PCB pins connected to the proper signals from the tester by Vision without having to solder wires to the Matrix Board.
The Matrix Board should dramatically reduce the labor hours and calendar time required to setup and test new designs. As a small company, Radiant cannot move forward in its pMEMS development without the functionality offered by such an automated test board.
Matrix Board

## Slide 25
Matrix Board
This is a very complex system for which development just started. It may not be successful!

## Slide 26
Conclusion
  Radiant recently processed its first piezoMEMS wafer through die-on-PCB.
  Each device type must now be tested and made to perform its targeted function.
  All die layouts were forced to fit onto a standard floorplan to ease the labor required to package and test each device type.
  New Vision Tasks are being written to characterize the electromechanical properties of the piezoMEMS.
  Four new instruments or fixtures are in development to support testing:
    PiezoMEMS Analyzer
    Precision Multiplexer
    LVH Temperature Component Test Fixture
    Test Matrix Board.